## Slide 1: Advanced Computer Architecture
Sandesh Shrestha
BEG478CO
Year: IV
Semester: II

## Slide 2: Advanced Computer Architecture
Board Exam Questions patterns
Total 10 questions and 8 questions to solve 10*8=80 marks
Students’ Work
It should consist of minimum 10-12 assignments with emphasis on solving problems.

## Slide 3: Reference Books :
Advanced computer architecture – Kai Hwang (MGH).
Computer Architecture and Parallel Processing – Kai Hwang And Briggs (MGH).
Advanced computer Architecture – Dezso Sima, Terence Fountain & Peter Kacsuk (Pearson Education)
Parallel Programming Techniques & Applications using Networked Worksataions & Parallel Computers-Barry Wilkinson & Michael Allen–Second Edition (Pearson Education).
Introduction to Parallel Processing – M. Sasikumar, D. Shikare & P. Ravi Prakash (PHI).
Internet for Open MP, Hadup and others.

## Slide 4: Course Objective
Learn and appreciate computer architecture with an emphasis on system design, performance and analysis.
Elevate thinking process to the level of performance improvement techniques for recent multi-core architecture.
Enable exploration of future directions in computer architecture research.

## Slide 5: 1.Concept
Original sense: – Taking a range of building materials, putting together in desirable ways to achieve a building suited to its purpose

## Slide 6
In Computer System:
Similar: how parts are put together to achieve some overall goal
Examples: the architecture of a chip, of the Internet, of an enterprise database system, an email system, a cable TV distribution system
Adapted from David Clark’s, What is “Architecture”?

## Slide 7: Role of Computer Architects
Applications and hand held devices are the part and parcel of our day to day life

## Slide 8: Why Computer Architecture?
Exploit advances in technology
  – Make things Faster, Smaller, Cheaper, …
Which enables new applications
– Life-like 3D games 15 years ago?
Make new things possible
  – Smart dust? Accurate one-month weather forecasts? Cure for cancer?
The advancement of computer architecture is vital for the advancement of all other areas of computing!

## Slide 9: Key Applications in the future decade
Agritronics (Smart Farming)

## Slide 10
Smart Health Care

## Slide 11
Smart Homes (Home Automation)

## Slide 12
Intelligent Transportation

## Slide 13
High Precision Security

## Slide 14
Weather Forecasting

## Slide 15: How are all these done?

## Slide 16: Review: Some Basic Definitions
Kilo byte – 210 or 1,024 bytes
Megabyte – 220 or 1,048,576 bytes
  – sometimes “rounded” to 106 or 1,000,000 bytes
Gigabyte – 230 or 1,073,741,824 bytes
  – sometimes rounded to 109 or 1,000,000,000 bytes
Terabyte – 240 or 1,099,511,627,776 bytes
  – sometimes rounded to 1012 or 1,000,000,000,000 bytes
Petabyte – 250 or 1024 terabytes
  – sometimes rounded to 1015 or 1,000,000,000,000,000 bytes
Exabyte – 260 or 1024 petabytes
  – Sometimes rounded to 1018 or 1,000,000,000,000,000,000 bytes

## Slide 17: Background
Transistor
Logic

## Slide 18: Transistor

## Slide 19: What’s the culprit in computer’s performance?

## Slide 20: Buffer

## Slide 21: Inverter

## Slide 22: NAND gate

## Slide 23: NOR gate

## Slide 24: What is Moore’s Law?
In 1965, Intel’s Gordon Moore predicted that the number of transistors that can be integrated on single chip would double about every two years.

## Slide 25: Technology Scaling Road Map (ITRS)
• Fun facts about 45nm transistors
  – 30 million can fit on the head of a pin – You could fit more than 2,000 across the width of a human hair
  – If car prices had fallen at the same rate as the price of a single transistor has since 1968, a new car today would cost about 1 cent

## Slide 26: What’s the other implication of Moore’s Law (1965)?
Transistors per inch square
  – Twice as many after ~1.5-2 years
Related trends
– Memory capacity
Twice as much in < 2 years
– Processor performance
Twice as fast after ~18 months

## Slide 27: Another Example of Moore’s Law Impact

## Slide 28: But What Happened to Clock Rates and Why?
Clock rates hit a “power wall”

## Slide 29
“For the P6, success criteria included performance above a certain level and failure criteria included power dissipation above some threshold.”
Bob Colwell, Pentium Chronicles

## Slide 30: How to use 1B (or more) transistors?
1. Instruction set architecture (ISA)
– interface between HW and SW
– different ISAs may be more/less effective for different target application areas
2. Microarchitecture
– Techniques below the ISA level (transparent)
– ex. pipelining, caching, branch prediction, superscalar, dynamic scheduling, clock-gating, …

## Slide 31: Performance Trend

## Slide 32: Price Trends

## Slide 33: Price Trends (DRAM memory)

## Slide 34: Why Do You Care About Prices?
Target market, target prices place a limit on the cost of my processor
– price = what I sell the part for
– cost = what it costs me
Design decisions affect the cost (and price)
– Ex. adding more cache may improve performance, but increase cost
Price-performance is often what we’re trying to balance

## Slide 35: Depends on the Class of Processor

## Slide 36: Desktop Systems
• Examples
– Intel Core 2 Duo
  – AMD Opteron
• Applications: everything (general purpose) – Office, Internet, Multi-media, Video Games…
• Goals
– performance, price/performance
– power affects cost, noise, size

## Slide 37: Servers
• Examples
  – IBM Power
  – Sun Niagara (T1)
  – Intel Xeon
• Applications
  – infrastructure: file server, email server, …
  – business: web, e-commerce, databases
• Goals
  – Throughput (transactions/second)
  – Availability (reliability, dependability, fault tolerance …)
– Cost not a major issue
  – But power is (power bill)

## Slide 38: Embedded
• Examples
  – Xscale, ARM, MIPS, x86, … (many varieties)
• Applications
  – cell phones, mp3 players, game consoles, consumer electronics (refrigerator, microwave), automobiles, … (many varieties)
• Goals
  – Cost, Power
  – Sufficient performance, real-time performance
  – Size (CPU size, memory footprint, chip count…)

## Slide 39: How to make a microprocessor chip?

## Slide 40: Silicon Ingot

## Slide 41: Czochralski Process

## Slide 42: Manufacturing ICs

## Slide 43: Silicon Wafer before processing

## Slide 44: Final Silicon Wafer

## Slide 45: Packaging
Signal and power connections between the chip and a circuit board
Remove heat produced from the chip
Protects from mechanical and thermal damage
Cost saving

## Slide 46: Fabrication Costs
• CPU (die) size greatly affects cost of all systems (desktop/server/embedded)
  – Current CPUs 1-2 cm2
  – Embedded much smaller
    • cost and footprint really matters in cell phone or iPod

## Slide 47: Impact of Die Size

## Slide 48: Yield

## Slide 49: Interaction of Price and Performance
• Add a new architectural feature to chip
  – for more performance, for less power, etc.
• Chip die size increases
  – Fewer dies per wafer
  – More defective dies
• Die testing more expensive
  – Must test whether feature works
• Die package more expensive
  – Larger package, maybe more pins
  – If feature needs more power, may need better heat sink

## Slide 50: Goal of Processor Design
• Maximize performance
  • Within the constraints of
    – Peak power, average power, thermals, die area, metal layers, reliability, manufacturing costs, implementation complexity, verification complexity, time-to-market, cost to manufacturer (Intel), cost to OEM (Dell), cost to end-customer (you).
    – Which really just says:
    • Maximize performance per $$$
•Huge, multi-variable optimization problem!
  – Not all variables are independent
  – Not all variables have the same weight
  – The same variable may have different weights to different customers
Laptop/Embedded: Power, weight and size constraints are more important than in Desktop/Server world

## Slide 51: Basic Computational Model

## Slide 55: Von-Neumann and Harvard Architecture
Two types of digital architectures
Classified by how they use memory

## Slide 56: Von-Neumann Architecture
The same memory and bus are used to store both data and instructions that run the program.
Since we cannot access program memory and data memory simultaneously, the Von Neumann architecture is susceptible to bottlenecks and the system performance is affected.
The processor needs two clock cycles to complete an instruction. So, pipelining is not possible with this architecture.
In the first clock cycle, the processor gets the instruction from memory and decodes it. In the next clock cycle the required data is taken from memory. For each instruction, this cycle repeats and hence needs two cycles to complete an instruction.
Von Neumann architecture is relatively older and was replaced by Harvard architecture.

## Slide 57: The Von Neumann Bottleneck
The Von Neumann bottleneck is a limitation of throughput caused by the standard personal computer architecture.
If a Von Neumann machine wants to perform an operation on some data in memory, it has to move the data across the bus into the CPU. When the computation is done, it needs to move outputs of the computation to memory across the same bus. The amount of data the bus can transfer at one time limit the speed and bandwidth of the system.
The processor can be idle while waiting for the memory fetch based on what the processor might need to do after the current operation is finished.
That limited throughput of a computer is referred to the Von Neumann bottleneck and often limits the performance of the system.

## Slide 58: Harvard Architecture
The name is originated from ‘Harvard Mark I’ a relay based old computer.
The Harvard architecture stores machine instructions (program) and data in separate memory units that are connected by different buses. It means it has two separate memories for storing data and program.
Processor can complete and instruction in one cycle if appropriate pipelining strategies are implemented. Or computers designed with Harvard architecture are able to run a program and access data independently, and therefore simultaneously.
Harvard architecture has a strict separation between data and code. Thus Harvard architecture is more complicated but separate pipelines remove the bottleneck that Von Neumann creates.

## Slide 59: Difference between Von Neumann and Harvard architecture
Von Neumann architecture | Harvard architecture
Named after the mathematician and early computer scientist John Von Neumann. | Name originated from ‘Harvard Mark I’, a relay based old computer.
Requires only one memory for their instruction. | Requires two memories for their instruction (program) and data.
Design is simple. | Complicated design.
Requires only one bus for instruction and data. | Requires separate bus for instruction and data.
Processor needs two clock cycles to complete an instruction. | Processor can complete an instruction in one cycle.
Low performance as compared to Harvard architecture. | Easier to pipeline, so high performance can be achieved.

## Slide 60: Difference between Von Neumann and Harvard architecture
Von Neumann architecture | Harvard architecture
Cheaper. | Comparatively high cost.
Used in microcontroller and signal processing. | Used in Laptop, personal computer and workstation.

## Slide 61: Questions?
shrestha.sandesh@khec.edu.np
sandeshshrestha45@gmail.com